## Slide 1: Csd (Canonical signed digit) based low power FIR filter design
Tools Used: Xilinx ISE Design Suite 12.3 MATLAB fdatool

## Slide 2
Mentor: Prof. R. Dwivedi
Students:
(08105EN063) Mukul Sharma
(08105EN064) Gaurav Verma
(08105EN069) Ajit Singh Songara

## Slide 3: Problem Description
Digital filters contain a great number of constant coefficient multipliers
Multipliers can be optimized by using CSD-encoding (Canonical Signed Digit) for low power/high performance.
Design 2 filter versions, one using 2’s complemented form and the other using CSD encoded coefficients, and compare their performance

## Slide 4: Tasks
Literature study of CSD-encoding.
Define a case; a filter with coefficient sets that shall be tested.
Develop CSD-encoding for the coefficient sets, code them in VHDL modules and test them through simulation.
Implementation of CSD-encoding based filter on FPGA.

## Slide 5: Canonical Signed Digit
The Canonical Signed Digit (CSD) number system is a signed digit number system that minimizes the number of non-zero digits.
This can be used to reduce the number of adds in a logic circuit.
The digit set is ternary and each digit can be either -1, 0. or +1.
CSD digits that are beside each other are never both = 1. This implies that for an n-bit number, there are at most [n/2] non-zero digits.

## Slide 6: Table : Three Digit Canonical Signed Digit Numbers

## Slide 7: Binary to CSD Algorithm

## Slide 8: Digital Filters
In a circuit one often wants to remove noise or extract useful parts of a signal.
To do this one uses filters. There are two kinds of filters, digital and analog.
Analog are built up by resistors, capacitors and op-amps. Analog filters are mathematically modeled using ordinary differential equations of Laplace transforms.
Digital filters perform numerical calculations on sampled values of a signal.

## Slide 9
Fig. : Basic setup of a digital filter

## Slide 10: Pros and Cons of Digital Filters
+ Digital filters can realize characteristics that is not so easily done by analog filters
+ Digital filters have the potential to attain a much better signal-to-noise ratio.
+ Digital filters are much easier to design, test and implement than an analog filter.
+ Digital filters can handle low frequency signals accurately
- Digital storage and computation limitations will give deterministic quantization errors after the ADC stage.

## Slide 11: Direct Form Filter
Fig. : Direct form FIR filter

## Slide 12
For an LTI (linear time invariant) FIR filter,

## Slide 13: Filter Characteristics

## Slide 14: Frequency Response of the designed filter
at Fs = 6000 HZ

## Slide 15: Digital Filter Coefficients
k | h(k)
0 | 0.002437094
1 | 0.013715162
2 | -0.044250023
3 | -0.044364337
4 | 0.28976238
5 | 0.5575594
6 | 0.28976238
7 | -0.044364337
8 | -0.044250023
9 | 0.013715162
10 | 0.002437094

## Slide 16: Up-scaled and Coded coefficients: CSD based
k | h(k) | h(k) scaled | h(k) rounded | h(k), 16 bit CSD encoded
0 | 0.002437094 | 24.37094 | 24 | 000000000010Ῑ000
1 | 0.013715162 | 137.15162 | 137 | 0000000010001001
2 | -0.044250023 | -442.50023 | -443 | 000000Ῑ001000101
3 | -0.044364337 | -443.64337 | -444 | 000000Ῑ001000100
4 | 0.28976238 | 2897.6238 | 2898 | 000Ῑ0Ῑ0101010010
5 | 0.5575594 | 5575.594 | 5576 | 0010Ῑ0Ῑ001001000
6 | 0.28976238 | 2897.6238 | 2898 | 00010Ῑ0Ῑ01010010
7 | -0.044364337 | -443.64337 | -444 | 000000Ῑ001000100
8 | -0.044250023 | -442.50023 | -443 | 000000Ῑ001000101
9 | 0.013715162 | 137.15162 | 137 | 0000000010001001
10 | 0.002437094 | 24.37094 | 24 | 000000000010Ῑ000

## Slide 17: Up-scaled and Coded coefficients: 2’s complement form
k | h(k) | h(k) scaled | h(k) rounded | h(k), 16 bit 2’s comp. encoded
0 | 0.002437094 | 24.37094 | 24 | 0000000000011000
1 | 0.013715162 | 137.15162 | 137 | 0000000010001001
2 | -0.044250023 | -442.50023 | -443 | 1111111001000101
3 | -0.044364337 | -443.64337 | -444 | 1111111001000100
4 | 0.28976238 | 2897.6238 | 2898 | 0000101101010010
5 | 0.5575594 | 5575.594 | 5576 | 0001010111001000
6 | 0.28976238 | 2897.6238 | 2898 | 0000101101010010
7 | -0.044364337 | -443.64337 | -444 | 1111111001000100
8 | -0.044250023 | -442.50023 | -443 | 1111111001000101
9 | 0.013715162 | 137.15162 | 137 | 0000000010001001
10 | 0.002437094 | 24.37094 | 24 | 0000000000011000

## Slide 18: Filter Schematic Diagram

## Slide 19: Mult. And Addn.

## Slide 20: Function Snippet

## Slide 21: Simulation

## Slide 22: RTL Schematic at Signal Level

## Slide 23: Schematic at Port Level

## Slide 24: Comparison of the two designed filters
Parameter | 2’s Complement | CSD Encoded
Maximum output required time after clock | 49.573ns | 38.687ns
Number of Slice Flip Flops | 103 out of 9,312 1% | 93 out of 9,312 1%
Number of 4 input LUTs | 747 out of 9,312 8% | 635 out of 9,312 6%
Power Consumption (in mW, at a clock of 40ns) | 102.53 | 101.33

## Slide 25
THANK YOU